|  | INTERCITY COACH – 12m / 12.80m |
| --- | --- |
|  |  |  | GENERAL FEATURES |
|  |  |  | Length | 11 995 mm | 12 760 mm |
|  |  |  | Width | 2 550 mm |
|  |  |  | Height with / without A/C | 3 455/3300 mm |
|  |  |  | Wheelbase | 6 200 mm | 6 965 mm |
|  |  |  | Front / rear overhang | 2 503 / 3 292 mm |
|  |  |  | Interior height clearance in the corridor | 2 275 mm |
|  |  |  | Floor height | 860 mm |
|  |  |  | Access height of front / centre doors | 344 / 344 mm |
|  | Layout maxi 12 m : 55 passenger seats (2001/85) |  | Width of front / centre doors* | 800 / 800 mm |
|  |  |  |  |  |  | Kerb-to-kerb turning radius | 9 400 mm | 10 150 mm |
|  |  |  | Wall-to-wall turning radius | 11 050 mm | 11 650 mm |
|  |  |  | Angle of attack / escape | 8°/8° |
|  |  |  | Maximum permitted weight on rear axle* | 11 500 kg |
|  |  |  | Maximum permitted weight on front axle | 7 100 kg |
|  |  |  | G.V.W.* | 18.000 kg |
|  |  |  | Capacity of the interior luggage compartment | 2.8 m3 | 3 m3 |
|  |  |  | Capacity of the luggage | 5.7 m3 | 6.7 m3 |
|  | Layout maxi 12.80 m : 59 passenger seats (2001/85) |  | * depends on local regulation and equipment of the vehicle |
|  |  |  |  |  |  |  | 194 kW (264 Hp) 220 kW (300 Hp) 243 kW (330Hp) 280 kW (380Hp) | Euro 5 EEV |

| CROSSWAY | 12m / 12.80m |
| --- | --- |
| ( BODYWORK / EXTERIOR EQUIPMENT Anticorrosion treatment by cataphoretic immersion, finished with a polyurethane resin final coat Exterior front and middle clearance door width 670 mm Side luggage compartment doors in pressed aluminum Optional*: Middle clearance door width 1200 mm Painting customization Labels "Transport of children" Upper rear light (direction & brake lights) ( INTERIOR EQUIPMENT Floor covered in self-adhesive anti-slip PVC Luggage racks above passenger seats Side walls in laminated panels Roof trim in laminated panels Dividing walls trimmed in laminate Automatic lighting of driver's compartment when doors are open 2 roof-mounted handrails Optional*: Central platform Wheelchair ramp with space to accommodate one wheelchair user (with middle door 1200 mm wide) Full height dividing wall behind the driver Curtains on side windows and rear glass Refrigerator integrated in the dashboard Request buttons to "STOP" (RADIO / VIDEO Optional*: Preparation for radio Complete installation for RADIO/CD Complete installation for VIDEO Microphone for driver ( ELECTRICAL EQUIPMENT 2 batteries 12 V - 170 Ah, mounted on a tray 2 alternators, 2 x 90 A Electrical box with fuses in the front left storage compartment Incandescent lighting of passenger compartment Fire detection system Optional*: 24 V socket on instrument panel Protection by thermal circuit breakers 230 A/h batteries 140 + 80 A Alternators Hazard warning lights activated when doors are opened Lighting in luggage compartment Reversing sensor system Lighting panels with neon tubes Front fog lamps ( WINDOWS / THERMAL COMFORT Tinted simple glass all round without ventilations 4 emergency exit windows ; 2 left and 2 right opaque roof hatches Thermal side, front panel & roof insulation Heating for passengers by 4 heaters Air extractor in the rear Electrical demisting of the front door Optional*: Side windows with tilting or sliding ventilations Double glazing of side windows; front door; driver’s side window Air conditioning without reheating function (roof unit) Air conditioning with reheating function (roof unit) Independent heating 30 kW 4 heaters for passengers with channels Demisting of front steps ( DRIVING POSITION Fully adjustable driver's air suspension seat with headrest, with 3 point seat belt Storage tray in central and side console Side/ front sun visor manually operated Exterior temperature indicator Engine rev counter Digital tachograph On-board computer (steering wheel controls) with fuel consumption control Optional*: Driver and passenger seats in same trim Driver luggage compartment rack with lock Hostess seat with 3 point safety belt 2 bottles refrigerated storage container Front sun visor electrically operated Alcohol Tester |  | ( ENGINE IVECO TECTOR EURO EEV diesel with 6 cylinders in line. Maximum power 194 kW (264 HP) at 2 200 – 2 500 rpm Maximum torque 1 000 Nm at 1 400 rpm Engine capacity 5.9 litres Cooling of the inlet air by air-air intercooler Electronic regulation Hydrostatic fan Cold start by means of a resistor integrated into the induction manifold Electric accelerator Optional*: IVECO TECTOR EEV with enhanced power Maximum power 220 kW (300 HP) at 2 300 – 2 500 rpm Maximum torque 1 050 Nm at 1 250 – 1 850 rpm IVECO CURSOR 8 EURO 5 diesel 6 cylinders in line ; 7.8 liters Maximum power 243 kW (330 HP) at 1 550 – 2 050 rpm Maximum torque 1 500 Nm at 1 125-1 550 rpm IVECO CURSOR 8 EURO 5 (SCR system) Maximum power 280 kW (380 HP) at 2 050 rpm Maximum torque 1 500 Nm at 1 125-1 550 rpm EEV (environmentally enhanced vehicle) exhaust emission standard ( GEARBOX 6 speed mechanical gearbox ZF Exterior warning buzzer with the shift of reverse speed Optional*: Automatic 4 speed VOITH D864.5 Automatic 6 speed ZF 6 HP or AsTronic ( DRIVE AXLE STANDARD axle ratio 5,29 (max speed 116 km/h) Single reduction rear axle Optional*: Other ratios available (please contact us) ( FRONT AXLE / STEERING Front axle with independent wheels suspension Hydraulic steering ZF (SUSPENSION Full air suspension with self-leveling sensor Front: 2 air springs /2 shock absorbers / 1 stabilization bar /1 leveling sensor Rear: 4 air springs/ 4 shock absorbers / 4 retaining rods /1 stabilization bar / 2 leveling sensors Optional*: Lifting / Lowering device of the vehicle suspension ( COMPRESSED AIR Dual cylinder air compressor 630 cm3 (pressure 9,5 bar) Integrated air dryer: Bleeding valves on the air tanks ( BRAKES Pneumatically-controlled service disc brakes in front and rear ABS (anti block system) ASR (anti-slip system) Parking brake: 2 cylinders Emergency brake : guaranteed by independent circuits Optional*: Vehicle immobilization when the front or middle doors are open Electronic control of vehicle stability (ESP) Electronic control of brakes (EBS) ( RETARDER Electromagnetic retarder controlled by the main brake (possible to disconnect for manual control) Optional*: Hydraulic integrated retarder Decompression engine brake ( Cursor only) ( FUEL TANK 220 liters diesel tank , inlet on the right side 60 liters AdBlue tank, inlet on the right side Optional*: Capacity of 340 liter diesel tank ( WHEELS AND TYRES 22,5x8,25-10-152 M 22 E wheel rims 295/80 R 22,5 tyres Spare wheel and carriers in the front overhang |

# Text boxes

* Offer of standard and optional equipments can be different on various markets.

For any clarification about possible equipments, please contact sales representatives.