|  | INTERCITY COACH – 10.60m |
| --- | --- |
|  |  |  | GENERAL FEATURES |
|  |  |  | Length | 10 655 mm |
|  |  |  | Width | 2 550 mm |
|  |  |  | Max. height with / without A/C | 3 455/3300 mm |
|  |  |  | Wheelbase | 5 300 mm |
|  |  |  | Front / rear overhang | 2 063 mm/ 3 292 mm |
|  |  |  | Front / rear tracking | 2 068 mm /1 814 mm |
|  |  |  | Interior height clearance in the corridor | 2 275 mm |
|  |  |  | Floor height | 860 mm |
|  |  |  | Access height of front/centre doors | 344 / 344 mm |
|  |  |  | Width of front / centre door* | 800 / 800 mm |
|  |  |  | Kerb-to-kerb turning radius | 8 850 mm |
|  |  |  | Wall-to-wall turning radius | 9 600 mm |
|  |  |  | Angle of attack / escape | 10°/ 8° |
|  | Layout maxi 10.60m 47 passenger seats (2001/85) |  | Maximum permitted weight on rear axle* | 11 500 kg |
|  |  |  | Maximum permitted weight on front axle | 7 100 kg |
|  |  |  | G.V.W.* | 18.000 kg |
|  |  |  | Capacity of the interior luggage compartment | 1.9 m3 |
|  |  |  | Capacity of the luggage compartment under the floor | 3.5 m3 |
|  |  |  | * depends on local regulation and equipment of the vehicle |
|  |  |  |  | 243 kW (330 ch) 280 kW (380 ch) | EEV | Euro 5 E E V |

| ARWAY | 10m60 |
| --- | --- |
| (BODYWORK / EXTERIOR EQUIPMENT Anticorrosion treatment by cataphoretic immersion, finished with a polyurethane resin final coat Exterior front and middle clearance door width 670 mm Side luggage compartment doors in pressed aluminum Optional*: Middle clearance door width 1200 mm Painting customization Labels "Transport of children" Upper rear light (direction & brake lights) ( INTERIOR EQUIPMENT Floor covered in self-adhesive anti-slip PVC Luggage racks above passenger seats Side walls in laminated panels Roof trim: laminated panels Dividing walls Automatic lighting of driver's compartment when doors are open 2 roof-mounted handrails Optional*: Central platform Wheelchair ramp with space to accommodate one wheelchair user (oblige Middle door 1200 mm) Full height dividing wall behind the driver Curtains on side windows and rear glass Refrigerator integrated in the dashboard Request buttons to "STOP" (RADIO / VIDEO Optional*: Preparation for radio Complete installation for RADIO/CD Complete installation for VIDEO Microphone for driver Microphone for driver + microphone for guide ( ELECTRICAL EQUIPMENT 2 batteries 12 V - 170 Ah, mounted on a tray 2 alternators, 90 A Front fog lamps Electrical box with fuses in the front left storage compartment Incandescent lighting of passenger compartment Interior lighting for passengers direct by fluorescent tubes Fire detection system Optional*: 24 V socket on instrument panel Protection by thermal circuit breakers 230 A/h batteries 140 + 80 A Alternators Hazard warning lights activated when doors are opened Lighting in luggage compartment Reversing sensor system Amplified interior lighting for passengers direct by fluorescent tubes Interior lighting for passengers indirect by fluorescent tubes FIPO, REVERSE DRIVE RADAR, REVERSE DRIVE ALARM HORN ( WINDOWS / THERMAL COMFORT Tinted simple glass all round without ventilations 4 emergency exit windows - non-opening ; 2 left and 2 right Opaque roof hatches Thermal side, front panel & roof insulation Heating for passengers Air extractor in the rear Electrical demisting of the front door Optional*: Side windows with tilting or sliding ventilations Double glazing of side windows; front door; driver’s side window Air conditioning without reheating function (roof unit) Air conditioning with reheating function (roof unit) Individual air outlets; reading lights placed above passengers seats Independent heating 30 kW 4 heaters for passengers with channels Demisting of front steps ( DRIVING POSITION Fully adjustable driver's air suspension seat with headrest, with 3 point seat belt Storage tray in central and side console Side/ front sun visor manually operated Exterior temperature indicator Digital tachograph On-board computer (steering wheel controls) with fuel consumption control Optional*: Driver and passenger seats in same trim Driver luggage compartment rack with lock Hostess seat with 3 point safety belt 2 bottles refrigerated storage container Front sun visor electrically operated Integral CRUISE CONTROL Hostess seat with fixed back, folding seat and 3 point seat belt Alcohol Tester |  | ( ENGINE Diesel 6 cylinders in line, inclined to the rear left. Direct injection. Maximum power 243 kW (330 HP) at 2 050 rpm Maximum torque 1 500 Nm (153mkg) at 1 125-1 550 rpm Engine capacity 7,8 liters Supercharged by variable geometry turbo compressor with cooling of the inlet air by air-air intercooler Electronic regulation and pump injectors Hydrostatic fan Oil heat exchanger (7,6 dm2) Cold start by means of a resistor integrated into the induction manifold Electric accelerator EURO 5 exhaust emission standard Optional*: Maximum power 280 kW (380 HP) at 2 050 rpm EEV exhaust emission standard ( GEARBOX 6 speed mechanical gearbox ZF Exterior warning buzzer with the shift of reverse speed Optional*: Automatic 4 speed VOITH D864.5 Automatic 6 speed ZF 6 HP Automated 12 speed ZF AsTronic (380 HP only) ( DRIVE AXLE Standard axle ratio 3,36 maximum speed: 118 km/h Single reduction rear axle Optional*: Other ratios related to the engine, gearbox and mission available ( FRONT AXLE / STEERING Front axle with independent wheels suspension Hydraulic steering (SUSPENSION Full air suspension with self-leveling sensor Front: 2 air springs /2 shock absorbers / 1 stabilization bar /1 leveling sensor Rear: 4 air springs/ 4 shock absorbers / 4 retaining rods /1 stabilization bar / 2 leveling sensors Optional*: Lifting / Lowering device of the vehicle suspension ( COMPRESSED AIR Dual cylinder air compressor 630 cm3 (pressure 9,5 bar) Integrated air dryer: Bleeding valves on the air tanks ( BRAKES Pneumatically-controlled service disc brakes in front and rear ABS (anti block system) ASR (anti-slip system) Parking brake: 2 cylinders Emergency brake : guaranteed by independent circuits Optional*: Vehicle immobilization when the front or middle doors are open Electronic control of vehicle stability (ESP) Electronic control of brakes (EBS) ( RETARDER Electromagnetic retarder controlled by the main brake (possible to disconnect for manual control) Decompression engine brake Optional*: Hydraulic integrated retarder ( FUEL TANK 350 liters diesel tank , inlet on the left and right side 60 liters AdBlue tank, inlet on the right side ( WHEELS AND TYRES 22,5x8,25-10-152 M 22 E wheel rims 295/80 R 22,5 tyres Spare wheel and carriers in the front overhang |

# Text boxes

* Offer of standard and optional equipments can be different on various markets.

For any clarification about possible equipments, please contact sales representatives.